The Grand I/O System

The grandios module in C is modeled directly on The MPS (Mobil Programming System) I/O Package described by Waite in Implementing Software for Non-Numeric Applications, Appendix A.

The F4IO Implementation
The MPS package was written in FORTRAN for portability. The implementation in Waite, called F4IO, provides four logical I/O channels that correspond to line (or record) oriented magnetic tape units in FORTRAN vocabulary. It was originally written in FORTRAN IV and conforms to the later FORTRAN 1966 standard. The four channels have the default properties shown in Table 1.

Channel Number	FORTRAN Unit	Default Use
1	5	Input
2	4	Scratch
3	7	Normal Output
4	6	Error Output

Table 1 – Default Channel Properties

The MPS design provides for the possibility of up to nine channels numbered 1 through 9. The grandios implementation, described later, adds the channels numbered 5 through 9 as additional scratch channels that can be configured for the needs of particular applications.

Each channel is configured by means of attributes that control the behavior of the channel for reading, writing, open, and control (such as write end-of-file or rewind), plus a status attribute that reflects the result of operations performed on the channel (such as open, close, or end of file reached).

These attributes are summarized in Table 2.

Read	0	Reading is illegal
	1	Read a line of characters assumed ≤ MAXLEN characters
Write	0	Writing is illegal
	1	Write a fixed length line of MAXLEN characters
	2	Write a variable length line of ≤ MAXLEN characters
	3	As 2 except that a FORTAN printer carriage control character is inserted
Open	0	No action is required
	1	The channel is rewound each time it is opened
Control	0	No control operations are available
	1	Open for reading until end of file is reached
	2	If open for writing an end-of-file mark is written
Status	0	The channel is not available
	1	The channel is closed
	2	The channel is open for reading
	3	The channel is open for writing
	4	The channel is open for both reading and writing
	5	An end-of-file or end-of-medium has been detected

Table 2 – Channel Attributes and Status Codes

The F4IO implementation provides a main program that initializes the channels as described in Table 1. Then it calls an application program which has the generic name PROGR. This external application program can be an implementation of the SIMCMP or STAGE2 macro processors, a test program, or any other application that makes use of the I/O module. When the PROGR application returns control to the main program it closes all the channels that accept the close operation.

The workhorse of F4IO is FUNCTION IOOP(JOP,JCH,JBA,JP1,JP2) where JOP is the operation code (-1 for read, 0 for control, 1 for write), JCH is the channel number, JBA is the array of characters for input or output, JP1 is the beginning index in JBA, and JP2 is the end index.

IOOP checks the operation requested for legality, opens the channel if needed, and routs the operation to another subroutine for read, write, or control. IOOP sets the status of the channel to reflect the success or failure of the operation and returns an error code shown in Table 3 if anything went wrong.

IOOP
0	Operation completed normally
1	End-of-file or end -of-medium was detected
2	Illegal operation on this channel
≥3	IOOP error code

Table 3 – IOOP Return Values

The Grand I/O System Implementation
The grandios implementation began as a port of F4IO by translating it to C and making some extensions to make it convenient to use on modern personal computers. Portability has been preserved by adhering strictly to ANSI Standard C. The number of channels has been expanded to ten, including channel number 0 as the null channel. Channel 0 was handled as a special case in F4IO. Channels 1 through 4 have the same default functionality as in Table 1, where now channel 1 maps to stdin, channel 3 to stdout, and channel 4 to stderr. Channel 2 can be used as a scratch file as well as the added channels 5 through 9. The channels can be attached to file names be position dependent command line arguments as in this example:

stg2 chan1.txt chan2.txt chan3.txt chan4.txt
If a channel position is to be skipped a – is put in its place. So, for example, if stage2 is to be run and no scratch channel is needed the command line would be:

stg2 chan1.txt - chan3.txt chan4.txt

In both of these examples it is assumed stage2 is compiled with the grandios module as its I/O system, chan1.txt is the file of stage2 macro definitions and macro calls, chan3.txt is the macro expansion output, and chan4.txt will contain any error messages.

Channel configuration is stored in a struct defined in grandios.h as follows:

struct CHAN {
    char r; /* read access */
    char w; /* write access */
    char o; /* open access */
    char c; /* control access */
    char s; /* status */
    FILE* fp; /* stream file pointer */
    char *pFile; /* pointer to filename */
};

Where the read, write, open, control, and status codes are as defined in Table 2. The stream file pointer fp is set when a file is opened on the channel, and pFile is a pointer to the filename, set when a filename is provided on the command line or by other means. The channel attributes are set to defaults in a struct declaration in grandios.c as follows:

struct CHAN chan[MAXCHAN+1] =
{
/* r w o c s fp pFile chan use stream */
    { 0, 0, 0, 0, 0, NULL, NULL }, /* 0 nullchan */
    { 1, 0, 0, 1, 1, NULL, NULL }, /* 1 input stdin */
    { 1, 1, 1, 2, 1, NULL, NULL }, /* 2 scratch */
    { 0, 1, 0, 2, 1, NULL, NULL }, /* 3 output stdout */
    { 0, 3, 0, 0, 1, NULL, NULL }, /* 4 error stderr */
    { 1, 1, 1, 2, 1, NULL, NULL }, /* 5 scratch */
    { 1, 1, 1, 2, 1, NULL, NULL }, /* 6 scratch */
    { 1, 1, 1, 2, 1, NULL, NULL }, /* 7 scratch */
    { 1, 1, 1, 2, 1, NULL, NULL }, /* 8 scratch */
    { 1, 1, 1, 2, 1, NULL, NULL }, /* 9 scratch */
};

Where MAXCHAN is defined as 9 in grandios.h.

The MPS design uses a LINE buffer to store the result of a read operation, and to accumulate the output for a write operation. The LINE buffer in C is an array of up to 120 ASCII characters, plus space for a newline character and a null terminating character, in other words, a total of up to 122 characters. Another line buffer called MB is used for formatted error messages in the Stage 2 macro processor.
Modification to Channel 1
In order to make Stage 2 more convenient as a compiler for Small I modified Channel 1, the input channel, so that when an input file given on the command line reaches end-of-file the input stream reverts to stdin. This makes it possible to run Stage 2 with macro definitions, such as small.s2m, given on the command line and a Small program, such as example.s1, read using redirected stdin on the command line. For example:

stg2 small.s2m <example.s1 – example.mill example.lss

In this example small.s2m is the set of macros that translate Small (simple mobile algorithmic language) to Mill (machine independent low level language), example.s1 is a source file of a program written in Small, example.mill is the channel 3 output containing the translation, and example.lss is a listing file showing any errors detected during processing. Please see the small repository (github.com/crandylb/small) for more examples or information about Small.

A further use of this modification is to make possible interactive applications of Stage 2. For example, Stage 2, like many other interpretive processors, is capable of being used as a desk calculator using a set of macros providing general or special purpose calculator functions.